## Slide 1
Tea Sense
NIR spectroscopy + AI for rapid tea testing
TEA SENSE: A Spectroscopic System for Estimating Moisture and Quality Parameters in Black Tea
Muhammed Saad Mazhar (IIT 20221804, UoW W2053223)
Supervisor: Mr. Ajeevan Sivanandhan
BSc (Hons) Computer Science, IIT / University of Westminster
RESEARCH QUESTION
Can a few seconds of near-infrared light, read by AI, replace hours of laboratory testing for screening black-tea moisture and quality?
Project Proposal live presentation • October 2026
FINAL YEAR PROJECT PROPOSAL · 2026/27
~6 h
oven-drying today
Seconds
per NIR scan
5
parameters assessed
Notes: Introduce yourself, supervisor and the one-line question. Hook: moisture testing alone takes about 6 hours in the oven; an NIR scan takes seconds. Say the plan: prove it on moisture, then map which other tea parameters are realistic.

## Slide 2
02 · AGENDA
Agenda and timing
Delivery/Q&A 30%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
02 / 23
20
minutes
23 slides in six sections. The talk ends at about 17.5 minutes, leaving time for questions.
01
Problem and aim
Problem, evidence, research questions, objectives
Slides 3 to 6
0 to 4 min
02
Literature
Review, parameter feasibility, existing solutions, gap
Slides 7 to 10
4 to 8 min
03
Solution and method
Solution, tools, methodology, evaluation, proof of concept
Slides 11 to 15
8 to 14 min
04
Project management
Ethics, schedule, risks
Slides 16 to 18
14 to 16.5 min
05
References and conclusion
Q1/Q2 references, closing statement
Slides 19 to 21
16.5 to 17.5 min
06
Questions
Q&A and thank you
Slides 22 to 23
17.5 to 20 min
Notes: Twenty slides in six sections; aim to finish the talk by 17.5 minutes Signal the structure: problem, aim, literature, solution, management, references Transition: "Let me start with why tea testing is slow."

## Slide 3
03 · PROBLEM
Problem context
Problem/aim/objectives 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
03 / 23
THE PROBLEM
Domain Black-tea quality control in Sri Lanka, which exported 257.44 million kg in 2025 (Daily FT, 2026)
Parameters Moisture, polyphenols, TF:TR ratio, caffeine, added sugar and glyphosate residues
Limitation Each needs its own laboratory method; oven-drying to constant mass takes about 6 h (ISO 1573)
Affected Factories, dryer operators, QC staff, brokers, the Tea Board and laboratories
Consequence Results arrive after drying, grading and trading decisions are made
Computing problem Turning noisy, high-dimensional NIR spectra into reliable estimates that hold on unseen tea
CONVENTIONAL TESTS VS NIR
Moisture
Oven-drying to constant mass; about 6 h; destructive
Polyphenols
Folin-Ciocalteu (ISO 14502-1); hours; reagents
TF and TR
Solvent extraction (Roberts and Smith, 1961)
Caffeine, sugars
HPLC after extraction
Glyphosate
LC-MS/MS after selective extraction (Wang et al., 2023)
NIR scan
Seconds; no reagents; the sample stays intact
KEY POINT
6 hours → seconds
One NIR spectrum carries O-H, C-H and N-H information about several components at once, so one scan could feed several AI models (Wang et al., 2025).
Notes: Walk left to right: who is affected, then the time cost of each test. Stress: the 6 h is the oven time in my own lab procedure; ISO 1573 only says "to constant mass". Computing angle: this is a signal-processing and generalisation problem, not just a gadget.

## Slide 4
04 · EVIDENCE
Evidence and problem statement
Problem/aim/objectives 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
04 / 23
PROBLEM STATEMENT
Black-tea quality is assessed with separate, slow, destructive laboratory methods, about six hours for moisture alone. There is a need to evaluate whether NIR spectroscopy with chemometric and AI models can estimate these parameters, starting with moisture, accurately and rapidly enough for screening, and to establish which further parameters such a framework can realistically estimate.
WHY IT MATTERS
Drying, release and adulteration decisions are made before laboratory results arrive, and existing NIR models have not been validated on Sri Lankan black tea.
EVIDENCE
01
Scale 257.44 million kg exported, about US$1.51 billion in 2025 (Daily FT, 2026)
02
Integrity Tea is a high-risk product for fraud and adulteration (Wu et al., 2027)
03
Slow methods Laboratory tests are reagent-heavy and unsuited to real-time control (Wang et al., 2025)
04
Single-site models Every NIR moisture study reviewed used one cultivar, site or season (Zou et al., 2022; Lan et al., 2022; Tao et al., 2026)
05
Overstated accuracy 98.3% in calibration vs 92.3% in validation (Revilla et al., 2024)
06
Poor generalisation A leaf-moisture model fell from Rp 0.903 to 0.138 in a new year (Liu et al., 2025)
Notes: Read the problem statement slowly; it is the anchor for everything after. Note: the 2025 export figure is 257.44 million kg; 245.79 million kg was 2024. Likely question: why not just buy an NIR analyser? Answer: proprietary calibrations, cost, and no local validation.

## Slide 5
05 · AIM AND RESEARCH QUESTIONS
Research aim and questions
Problem/aim/objectives 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
05 / 23
AIM
Design, develop and evaluate a near-infrared spectroscopy and AI framework for rapid, non-destructive estimation of black-tea quality parameters: validated experimentally on moisture, and assessed by evidence synthesis for polyphenols, TF:TR, caffeine, added sugar and glyphosate.
RQ1
To what extent can NIR spectra predict the moisture of Sri Lankan black tea against oven-drying on unseen samples?
Experiment
RQ2
How do preprocessing (SNV, MSC, Savitzky-Golay) and wavelength selection (CARS, SPA / iPLS) affect accuracy?
Experiment
RQ3
Do machine-learning models (SVR, RF) outperform PLSR, and do they hold on an unseen source?
Experiment
RQ4
How much measurement time is saved against oven-drying, and does accuracy hold in the field?
Experiment
RQ5
Which further parameters can one NIR framework realistically estimate?
Evidence synthesis
HOW THEY ARE ANSWERED
RQ1 to RQ4: a quantitative experiment on moisture. RQ5: an evidence-graded feasibility synthesis of Q1/Q2 literature (slide 8).
Notes: Read the main question first, then RQ1 to RQ5 RQ1 to RQ4 are experimental on moisture; RQ5 is evidence synthesis Likely question: "Why only moisture experimentally?" Oven and balance are the only in-house reference methods Transition: "Each question maps to objectives."

## Slide 6
06 · OBJECTIVES AND SCOPE
Objectives and scope
Problem/aim/objectives 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
06 / 23
OBJECTIVES, MAPPED TO RESEARCH QUESTIONS
O1
Review NIR, chemometrics and AI for tea parameters
RQ5
O2
Collect NIR spectra and triplicate oven moisture, 80 to 120 samples
RQ1
O3
Compare SNV, MSC and Savitzky-Golay preprocessing
RQ2
O4
Compare CARS with SPA / iPLS wavelength selection
RQ2
O5
Compare PLSR, SVR and RF; optional neural network
RQ3
O6
Evaluate on held-out and unseen-source samples
RQ1, RQ3
O7
Field-test the prototype against an oven-checked subset
RQ4
O8
Build a feasibility map for five further parameters
RQ5
SCOPE
IN
Portable 900 to 1700 nm NIR on Sri Lankan made black tea
IN
Full experiment for moisture; prototype with value, interval and flag
OUT
Certified results or regulatory claims
OUT
New reference chemistry for other parameters
OUT
Glyphosate detection by NIR
SUCCESS CRITERIA
R2p ≥ 0.90
RPD ≥ 2.5
RMSEP ≤ 0.5%
< 60 s / sample
On held-out samples, against about 6 h by oven; field error within 1.5 times lab error.
Notes: Point out the RQ tag on each objective: every RQ has at least one objective Scope: screening estimates, not certified results; no glyphosate by NIR Success criteria are fixed before data collection (R2p 0.90, RPD 2.5, under 60 s)

## Slide 7
07 · LITERATURE REVIEW
Background review
Background review 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
07 / 23
32
journal articles kept, all in Q1 or Q2 journals (SCImago)
REVIEW METHOD
Sources Google Scholar, ScienceDirect, MDPI, SpringerLink, PMC, RSC, Crossref
Search Tea AND parameter AND NIR AND modelling; 2016 to 2026 plus seminal methods
Screening Title, abstract, full text; SCImago Q1 or Q2 only
Flow 45 records; 5 off-domain and 14 below Q2 removed; 7 Q1/Q2 added
THEMES FROM THE LITERATURE
01
Moisture Strongest NIR target: Rp 0.971 (Bai et al., 2022); deep models on 17,856 line samples (Tao et al., 2026)
02
Phenolics Feasible but harder: TF:TR R2p 0.893, RPD above 3 (Dong et al., 2018); polyphenols only Rp 0.795 (Bai et al., 2022)
03
Caffeine Consistently strong: r2 0.97 against HPLC (Rehman et al., 2020)
04
Sugar and residues No Q1/Q2 NIR study of added sugar in black tea; glyphosate needs LC-MS/MS (Wang et al., 2023)
05
Preprocessing CARS kept 11 wavelengths for TF:TR (Dong et al., 2018)
06
Closest work Grades black tea from NIR + vision, not parameter values (Liang et al., 2025)
Moisture is the right experimental core; caffeine and TF:TR are the strongest extensions; glyphosate needs a different technology.
Notes: Synthesise, do not narrate papers: one sentence per theme. Contradiction to mention: the same spectra gave Rp 0.971 for moisture but 0.795 for polyphenols (Bai et al., 2022).

## Slide 8
08 · PARAMETER FEASIBILITY
What NIR can and cannot measure
Background review 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
08 / 23
PARAMETER
EVIDENCE FROM Q1/Q2 JOURNALS
VERDICT
Moisture
Strong O-H water bands; Rp 0.971 (Bai et al., 2022); all processing stages (Zou et al., 2022)
High · experimental core
Caffeine
r2 0.97 against HPLC (Rehman et al., 2020); predicted in black tea (Zareef et al., 2018)
High · extension
TF:TR ratio
R2p 0.893, RPD above 3 from 11 CARS wavelengths (Dong et al., 2018)
High · priority extension
Polyphenols
Rp 0.795 from NIR alone (Bai et al., 2022); RPD 5.4 fused with vision (Wang et al., 2021)
Medium to high
Added sugar
No Q1/Q2 NIR study in black tea; natural sugars vary (Piyasena et al., 2022)
Low to medium · evidence gap
Glyphosate
Trace residue at mg/kg; LC-MS/MS after selective extraction (Wang et al., 2023)
Not feasible by NIR
IMPLICATION
One scan can feed several models, but each parameter needs its own reference data and validation. Tea Sense validates moisture first and maps the rest.
Notes: This slide answers RQ5 at proposal stage All evidence is from Q1/Q2 journals Stress the honest negatives: no Q1/Q2 NIR study of added sugar in black tea; glyphosate needs LC-MS/MS Likely question: "Why include parameters you will not test?" To produce a feasibility map that guides future work Transition: "So what do existing tools already offer?"

## Slide 9
09 · EXISTING SOLUTIONS
Similar applications and existing solutions
Background review 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
09 / 23
SOLUTION
STRENGTH
LIMITATION
Oven-drying and wet chemistry
Accurate reference
Hours per parameter; destructive
Halogen moisture analysers
Minutes
Destructive; moisture only
Capacitive moisture meters
Instant and cheap
Sensitive to packing; no other parameters
In-line NIR analysers
Continuous monitoring
Costly; proprietary calibrations (Tao et al., 2026)
Handheld NIR research tools
Portable
Tested on one tea and site (Li et al., 2023; Tang et al., 2025)
Research NIR models
Accurate per parameter
Not Sri Lankan; time saving unmeasured
WHAT THIS TELLS US
01
Fast tools exist, but none combine speed, several parameters and low cost
02
Research accuracy is high but rarely validated across sources
03
No study reports time saved against oven-drying
04
Tea Sense: low-cost portable NIR, cross-source validation, measured time, flagged uncertainty
CLOSEST STUDY
Zou et al. (2022): black-tea moisture with a 77 g micro-NIR; SVR beat PLS. One cultivar; no time or field evaluation; not Sri Lankan tea.
The gap is not speed alone: it is speed, several parameters, low cost and validation across sources together.
Notes: Frame each solution as strength then limitation. Land on the closest study (Zou et al., 2022) and say exactly how Tea Sense differs.

## Slide 10
10 · GAP AND REQUIREMENTS
Research gap and solution requirements
Requirements 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
10 / 23
RESEARCH GAPS
G1
No validated NIR moisture model for Sri Lankan black tea
G2
Best preprocessing and wavelength selection unknown for this task
Dong et al., 2018; Liu et al., 2025
G3
Calibration does not guarantee generalisation
Revilla et al., 2024; Liu et al., 2025
G4
Time saving and field robustness rarely measured
G5
No consolidated view of which tea parameters one NIR framework can cover
The gap is not that NIR has never been used on tea; it is missing local, validated, time-measured evidence.
REQUIREMENTS (MOSCOW)
R1
Three referenced NIR scans and triplicate oven moisture
Must
R2
Test set locked before modelling; same splits for all models
Must
R3
R2p ≥ 0.90 and RPD ≥ 2.5 on held-out samples
Must
R4
Under 60 s from scan to result
Must
R5
Out-of-range flag and "screening estimate" label
Must
R6
One model per parameter in a shared registry
Must
R7
SUS ≥ 68 in field use
Should
TRACEABILITY
R2 answers G3, R4 answers G4 and R6 answers G5. The full list with verification methods is in the proposal (Appendix G).
Notes: Read the last line of the gap aloud; examiners often push on novelty. Show how requirements come from gaps, not from preference.

## Slide 11
11 · PROPOSED SOLUTION
Proposed solution overview
Proposal logic · Supports criteria
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
11 / 23
One scan, one model per parameter: a shared-spectrum NIR and AI framework that returns a screening estimate in seconds.
1
Log and seal the sample
2
Three referenced NIR scans, averaged
3
Oven-dry in triplicate (reference)
4
Preprocess: SNV, MSC, Savitzky-Golay
5
Select wavelengths: CARS vs SPA / iPLS
6
Model registry: PLSR, SVR, RF
7
Locked, unseen-source and field tests
8
Prototype: value, interval, flag
INPUT
Portable NIR spectrum (900 to 1700 nm) plus sample metadata
OUTPUT
Value, uncertainty interval, out-of-range flag and a "screening estimate" label
EXTENSIONS
Polyphenols, TF:TR, caffeine and sugar models added when partner-lab data exist; glyphosate routed to a separate residue test
ALREADY DEMONSTRATED
Runs end to end on public NIR moisture data: SVR RMSEP 1.04%, R2p 0.989 (surrogate data, not tea; slide 15).
Hardest part: generalising across sources with only 80 to 120 samples.
Notes: Walk the 8 pipeline steps; point out steps 3 and 7 as where the research rigour sits. Technically hardest: generalisation with a small dataset, which is why the evaluation is strict.

## Slide 12
12 · TOOLS AND TECHNOLOGIES
Tools, technologies and alternatives
Tools/technologies 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
12 / 23
DECISION
CHOICE, OVER ALTERNATIVES
Sensor
NIR, over UV-Vis, FTIR, THz (blocked by water), LIBS (destructive) and SERS (trace residues only)
Spectrometer
Portable 900 to 1700 nm InGaAs, over benchtop FT-NIR (cost, field use)
Reference
Oven-drying, over Karl Fischer (reagents) and halogen analysers
Preprocessing
SNV, MSC and Savitzky-Golay compared (Wang et al., 2025)
Wavelengths
CARS, with SPA / iPLS as comparators (Dong et al., 2018)
Models
PLSR baseline; SVR and RF; neural network only above about 150 samples
Software
Python and scikit-learn over MATLAB (licence); Git, MLflow, Streamlit
SELECTION CRITERIA
✓
Sensitivity to water and major tea components
✓
Portability and low cost for factories
✓
Evidence of use on tea
✓
Accuracy with small datasets
✓
Reproducibility and open licences
✓
Fit with the evaluation design
WHY NOT DEEP LEARNING FIRST?
Deep models won with 1,505 to 17,856 spectra (Kang et al., 2026; Tao et al., 2026). With 80 to 120 samples, PLSR, SVR and RF are the fair choices.
Notes: Every choice has a rejected alternative and a reason; say the reason, not the tool name. If asked about deep learning, use the yellow box.

## Slide 13
13 · METHODOLOGY
Methodology and methods
Methodology 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
13 / 23
Protocol and pilot
→
Collect
→
QC
→
Lock test set
→
Baseline
→
Preprocess
→
Select
→
Model
→
Evaluate
→
Field test
METHODOLOGY
Philosophy Positivism; deductive approach
Strategy Quantitative experiment on moisture plus structured evidence synthesis for other parameters
Development Iterative CRISP-DM cycle in two-week iterations
Hypotheses H1 to H5, tested against criteria fixed in advance
METHODS
Samples 80 to 120 Sri Lankan black teas from several sources; drying-stage and conditioned samples widen the range
Reference Oven-drying at 103 C to constant mass, in triplicate (SD ≤ 0.2%)
Scans White and dark references; three repacked scans
Split Kennard-Stone 70:30 locked test; leave-one-source-out
Tuning Nested 10-fold cross-validation on calibration data only
LEAKAGE CONTROL
Preprocessing, CARS and tuning are fitted inside cross-validation; repeat scans of a sample never cross sets; the test set is hashed and used once.
Notes: Distinguish methodology (how evidence is produced) from development process (how the pipeline is built). Mention the narrow made-tea moisture range and how conditioning widens it.

## Slide 14
14 · EVALUATION
Evaluation approach
Methodology 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
14 / 23
QUESTION
WHAT IS MEASURED
RQ1 Accuracy
RMSEP, R2p, RPD and bias on the locked test set
RQ2 Pipeline
RMSECV per preprocessing and selection option; band stability
RQ3 Models
SVR and RF vs PLSR (paired Wilcoxon); unseen-source error
RQ4 Speed
Seconds per sample vs oven time; field RMSEP; SUS
RQ5 Scope
Evidence-graded feasibility matrix
Baselines
Mean-only and PLSR on raw spectra; ablations remove each component
If AI does not beat PLSR, that is a valid finding and will be reported.
SUCCESS LEVELS
MINIMUM
R2p
≥ 0.80
RPD
≥ 2.0
TARGET
R2p
≥ 0.90
RPD
≥ 2.5
RMSEP
≤ 0.5%
Speed target: under 60 s per sample, against about 6 h by oven.
Notes: This is the slide examiners scrutinise most: tie every metric to an RQ. Be honest about the proof of concept: meat spectra (Borggaard and Thodberg, 1992), wider moisture range, different instrument. It shows the code and leakage-safe protocol work, and that SNV, CARS and SVR behave as the literature predicts.

## Slide 15
15 · PROOF OF CONCEPT
Preliminary proof of concept
Methodology 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
15 / 23
SET-UP (SURROGATE DATA)
Data Public Tecator NIR moisture data: 240 samples, 850 to 1050 nm (Borggaard and Thodberg, 1992)
Split Kennard-Stone: 168 calibration, 72 locked test
Pipeline SNV and Savitzky-Golay; CARS; PLSR, SVR, RF; 10-fold CV
Caveat Meat, not tea: this proves the pipeline, not tea performance
WHY IT MATTERS
The full pipeline, from preprocessing to locked-test evaluation, already runs, so tea data can be modelled as soon as it is collected.
1.04%
SVR RMSEP
0.989
SVR R2p
9.6
RPD
11 / 100
wavelengths kept by CARS
RMSEP ON THE LOCKED TEST SET (% MOISTURE; LOWER IS BETTER)
Mean-only baseline
10.36%
PLSR
1.92%
CARS-PLSR (11 bands)
1.96%
Random Forest
1.30%
SVR
1.04%
SVR beat PLSR (paired Wilcoxon p < 0.001) at 1.46 ms per prediction, against about 6 h for oven-drying.
Notes: Surrogate data (Tecator meat NIR), not tea: say this first The point is that the full pipeline already runs end to end SVR beat PLSR here; the real tea data may differ, and that is acceptable Transition: "Now the responsibilities that come with it."

## Slide 16
16 · ETHICS AND SUSTAINABILITY
Ethics, legal, social and sustainability
Ethics/impact 10%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
16 / 23
ISSUES AND SAFEGUARDS (BCS CODE OF CONDUCT)
Public interest
RISK
A screening estimate could release mouldy tea
SAFEGUARD
Value, interval and out-of-range flag; laboratory confirmation
Integrity
RISK
Overclaiming results
SAFEGUARD
Locked test set; negative results reported; no glyphosate claims
Duty to authority
RISK
Supplier confidentiality
SAFEGUARD
Coded sources; written consent
Legal
RISK
Sri Lanka PDPA No. 9 of 2022; open-source licences
SAFEGUARD
No personal data in the dataset
EDI
RISK
Smaller producers may be under-sampled
SAFEGUARD
Per-source error reported; Sinhala and Tamil labels as future work
Generative AI
RISK
Over-reliance on AI drafting
SAFEGUARD
Drafting and search support only; every citation verified; AI-use register
SUSTAINABILITY AND SDGS
9
SDG 9
Low-cost sensing and AI for tea processing
12
SDG 12
Less waste from testing and mis-dried tea
8
SDG 8
Value in Sri Lanka's export industry
No reagents, no sample destroyed, fewer oven runs; small models on a laptop CPU.
ETHICS STATUS
Low risk: no personal data; anonymous informed consent for field users; approval before any data collection.
Notes: Lead with the real harm: mouldy tea released because of a wrong low reading. Mention the AI-use register openly; it is part of professional integrity.

## Slide 17
17 · SCHEDULE
Time schedule and milestones
Time schedule 5%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
17 / 23
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
2026
2027
P1
Research and proposal
P2
Ethics, protocol and pilot
P3
Moisture data collection
P4
Cleaning and baseline
P5
Multi-parameter feasibility
P6
Preprocessing and selection
P7
Model development
P8
Evaluation and prototype
P9
Field feasibility
P10
Write-up and viva
MILESTONES
31 Oct
Proposal
30 Nov
Ethics and SOPs
15 Feb
Dataset ≥ 80
28 Feb
Test set locked
20 Apr
Evaluation
15 May
Final thesis
CRITICAL PATH
Data collection (gold) depends on spectrometer access and suppliers. Baseline modelling starts on early batches; 2 to 3 weeks of contingency sit in P10. Fortnightly supervisor meetings; weekly Gantt review.
Notes: Point to the critical path and the contingency, not every phase. Dates are indicative until checked against official IIT and UoW deadlines.

## Slide 18
18 · RISKS
Risks and mitigation
Schedule/risk 5%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
18 / 23
RISK
LIKELIHOOD
IMPACT
RESPONSE
Spectrometer unavailable
Confirm access by mid-November; benchtop fallback
Medium
High
Too few samples or narrow moisture range
Several suppliers and conditioning; accept 80 samples; drop the neural network
Medium
High
Inconsistent oven reference values
Written SOP, pilot and triplicates; re-run if SD > 0.2%
Medium
High
Data leakage inflating results
Hashed locked test set; scikit-learn pipelines
Medium
High
No partner lab for other parameters
Early outreach; evidence-only route already planned
High
Medium
Scope creep to all parameters
MoSCoW; moisture-first agreed with supervisor
High
High
Field conditions reduce accuracy
Log conditions; report as a feasibility finding
High
Medium
Weak or negative results, for example AI not beating PLSR, are reported as findings rather than hidden.
Notes: Each risk on the left lines up with its response on the right. Biggest risk: spectrometer access; say the fallback clearly.

## Slide 19
19 · REFERENCES
References (1 of 2)
References 5%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
19 / 23
JOURNAL ARTICLES · ALL IN Q1 OR Q2 JOURNALS (SCIMAGO) · HARVARD STYLE
Bai, X. et al. (2022)
Near-infrared spectroscopy and machine learning-based technique to predict quality-related parameters in instant tea. Scientific Reports, 12, 3833. https://doi.org/10.1038/s41598-022-07652-z
Borggaard, C. and Thodberg, H.H. (1992)
Optimal minimal neural interpretation of spectra. Analytical Chemistry, 64(5), pp.545-551. https://doi.org/10.1021/ac00029a018
Dong, C. et al. (2018)
Rapid determination by near infrared spectroscopy of theaflavins-to-thearubigins ratio during Congou black tea fermentation process. Spectrochimica Acta Part A: Molecular and Biomolecular Spectroscopy, 205, pp.227-234. https://doi.org/10.1016/j.saa.2018.07.029
Lan, T. et al. (2022)
A rapid prediction method of moisture content for green tea fixation based on WOA-Elman. Foods, 11(18), 2928. https://doi.org/10.3390/foods11182928
Li, L. et al. (2023)
Rapid and comprehensive grade evaluation of Keemun black tea using efficient multidimensional data fusion. Food Chemistry: X, 20, 100924. https://doi.org/10.1016/j.fochx.2023.100924
Liang, J. et al. (2025)
A black tea quality testing method for scale production using CV and NIRS with TCN for spectral feature extraction. Food Chemistry, 464, 141567. https://doi.org/10.1016/j.foodchem.2024.141567
Liu, H. et al. (2025)
Improvement method for tea leaf moisture content prediction using VIS-NIR spectrum based on transfer learning. Spectrochimica Acta Part A: Molecular and Biomolecular Spectroscopy, 343, 126571. https://doi.org/10.1016/j.saa.2025.126571
Liu, Y. et al. (2024)
Simultaneous determination of four catechins in black tea via NIR spectroscopy and feature wavelength selection: a novel approach. Sensors, 24(11), 3362. https://doi.org/10.3390/s24113362
Piyasena, K.G.N.P. et al. (2022)
Evaluation of inherent fructose, glucose and sucrose concentrations in tea leaves (Camellia sinensis L.) and in black tea. Applied Food Research, 2, 100100. https://doi.org/10.1016/j.afres.2022.100100
Rehman, N.U. et al. (2020)
FT-NIRS coupled with PLS regression as a complement to HPLC routine analysis of caffeine in tea samples. Foods, 9(6), 827. https://doi.org/10.3390/foods9060827
Revilla, I. et al. (2024)
The potential use of near infrared spectroscopy (NIRS) to determine the heavy metals and the percentage of blends in tea. Foods, 13(3), 450. https://doi.org/10.3390/foods13030450
Notes: Harvard style; journal names in italics Every journal article is in a Q1 or Q2 journal (SCImago); quartiles listed in Appendix A, Table A2 of the proposal Do not read the list; pause for 5 seconds, then move on

## Slide 20
20 · REFERENCES
References (2 of 2)
References 5%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
20 / 23
JOURNAL ARTICLES (CONTINUED)
Roberts, E.A.H. and Smith, R.F. (1961)
Spectrophotometric measurements of theaflavins and thearubigins in black tea liquors in assessments of quality in teas. The Analyst, 86(1019), pp.94-98. https://doi.org/10.1039/AN9618600094
Tang, J. et al. (2025)
Spectral multi-scale attention fusion network for rapid detection of black tea adulteration using a handheld spectrometer. Foods, 14(24), 4261. https://doi.org/10.3390/foods14244261
Tao, W. et al. (2026)
Deep learning model for real time moisture content detection and prediction in white tea withering using near infrared spectroscopy. Scientific Reports, 16, 26972. https://doi.org/10.1038/s41598-026-57739-0
Wang, Q. et al. (2023)
Development of a specific and sensitive method for the detection of glyphosate pesticide and its metabolite in tea using dummy molecularly imprinted solid-phase extraction coupled with liquid chromatography-tandem quadrupole mass spectrometry. Journal of Chromatography A, 1705, 464209. https://doi.org/10.1016/j.chroma.2023.464209
Wang, S. et al. (2025)
A review: integration of NIRS and chemometric methods for tea quality control: principles, spectral preprocessing methods, machine learning algorithms, research progress, and future directions. Food Research International, 205, 115870. https://doi.org/10.1016/j.foodres.2025.115870
Wang, Y. et al. (2021)
Enhanced quality monitoring during black tea processing by the fusion of NIRS and computer vision. Journal of Food Engineering, 304, 110599. https://doi.org/10.1016/j.jfoodeng.2021.110599
Wu, X. et al. (2027)
Authentication and traceability of tea as a high-risk product: a comprehensive review of spectroscopic and chemometric solutions. Food Control, 192, 112555. https://doi.org/10.1016/j.foodcont.2026.112555
Zareef, M. et al. (2018)
Prediction of amino acids, caffeine, theaflavins and water extract in black tea using FT-NIR spectroscopy coupled chemometrics algorithms. Analytical Methods, 10(25), pp.3023-3031. https://doi.org/10.1039/C8AY00731D
Zou, H. et al. (2022)
Prediction method of the moisture content of black tea during processing based on the miniaturized near-infrared spectrometer. Horticulturae, 8(12), 1170. https://doi.org/10.3390/horticulturae8121170
STANDARDS, PROFESSIONAL CODES AND DATA SOURCES (NOT JOURNAL ARTICLES)
BCS (n.d.) BCS, The Chartered Institute for IT. BCS Code of Conduct. Available at: https://www.bcs.org/membership-and-registrations/become-a-member/bcs-code-of-conduct (Accessed: 19 October 2026).
Daily FT (2026) Tea exports top $1.5 b in 2025 despite price pressures. 23 January. Available at: https://www.ft.lk/front-page/Tea-exports-top-1-5-b-in-2025-despite-price-pressures/44-787299 (Accessed: 19 October 2026).
ISO (1980) ISO 1573:1980 Tea: determination of loss in mass at 103 C. Geneva: International Organization for Standardization.
ISO (2005) ISO 14502-1:2005 Determination of substances characteristic of green and black tea, Part 1: content of total polyphenols in tea. Geneva: ISO.
Notes: Standards and the export statistic are not journal articles; they define reference methods and context Full list (33 journal articles) is in the proposal Transition: "To close..."

## Slide 21
21 · CONCLUSION
Delivery/Q&A 30%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
21 / 23
Closing statement
Seconds of light, instead of hours of drying.
Tea Sense tests whether that promise holds for Sri Lankan black tea, honestly and on unseen samples.
01
Addresses slow, fragmented tea quality testing: oven moisture takes about six hours.
02
Proposes a shared-spectrum NIR and AI framework, validated on moisture.
03
Uses a quantitative experiment plus a structured evidence synthesis of Q1/Q2 literature.
04
Evaluates with held-out and unseen-source RMSEP, R2p, RPD, bias and time per sample.
05
Delivers a dataset, models, a prototype and a feasibility map for five further parameters.
Notes: Slow down here: this is the summary the examiners will remember Read the quote, pause, then walk through the five points Transition: "I would be glad to take your questions."

## Slide 22
22 · QUESTIONS
Delivery/Q&A 30%
TEA SENSE
Muhammed Saad Mazhar · IIT 20221804 / UoW W2053223 · Final Year Project Proposal 2026/27
22 / 23
Q&A
Questions and discussion
I welcome questions on the method, the evidence and the plan.
PREPARED TO DISCUSS
Why moisture first?
Strongest NIR signal, and the oven reference is available in-house.
Why not glyphosate by NIR?
Trace residue with no NIR signal; it needs LC-MS/MS (Wang et al., 2023).
Why PLSR as the baseline?
The standard, well-understood model for small spectral datasets.
How is leakage prevented?
A locked, hashed test set; all tuning inside cross-validation.
What is the biggest risk?
Spectrometer access; a benchtop instrument is the fallback.
Notes: Leave this slide up for the whole Q&A The five prepared answers are on screen; expand on whichever is asked If asked about results: stress that the proof of concept used surrogate data, not tea If asked about sugar: no Q1/Q2 NIR study exists for added sugar in black tea, which is why it is graded low to medium

## Slide 23
23 · THANK YOU
Thank you
Tea Sense: NIR spectroscopy and AI for rapid tea testing
Muhammed Saad Mazhar
IIT 20221804 · UoW W2053223
Supervisor: Mr. Ajeevan Sivanandhan
BSc (Hons) Computer Science, IIT / University of Westminster
Notes: Thank the panel and the supervisor Keep this slide up only briefly if Q&A has already happened